BBT ANTENNAS INC

Model NO: BBT-2458PA1719R065-N4

Type ：MIMO sector panel Antenna

Application:

★2.4G/5.8G wireless coverage transmission system

★Point to point，point to multi-point MIMO system

★For WLAN、WIFI、WIMAX system

Features：

★Adopt Dual band/multi-port design,high gain、high transmission speed、good performance

★Strong anti-interference ability

Specifications:

| Electrical |
| --- |
| Model Number | BBT-2458PA1719R065-N4 |
| Frequency Range | 2400-2500MHz | 5150-5850MHZ |
| Polarization Type | ±90° |
| Gain | 17dBi | 19dBi |
| 3dB Beam-Width. H-Plan | 65° | 65° |
| 3dB Beam-Width. E-Plan | 7° | 5° |
| VSWR | ≤1.7 |
| Front to back Ratio | ≥23dB |
| Input Impedance | 50Ω |
| Max Input Power. | 50W |
| Lightning Protection | DC Grounded |
| Mechanical |
| Connector Type | 4×N-Type Female |
| Dimensions H*W*D (mm) | 870*280*80（mm） |
| Radome Material | PVC |
| Radome color | gray |
| Operating Temperature Rang | -40ºC/+60ºC |
| Support Pole Diameter | φ30-φ60(mm) |
| Rated Wind Velocity | 60m/s |

VSWR:

Radiation Pattern:

2400-2500MHz

5150-5850MHz

BBT ANTENNAS INC

Tel:(8620)38867118  Fax:(8620)38860481   http://www.bbtantennas.com