BBT ANTENNAS INC

Part NO.: BBT-RFID09C08-180

Type : RFID Antenna

Application:

Features:

Specifications:

| Electrical |
| --- |
| Part Number | BBT-RFID09C08-180 |
| Frequency Range | 902-928MHz |
| Polarization Type | RHCP |
| Gain | 8dBi |
| 3dB Beam-Width. H-Plan | 65° |
| 3dB Beam-Width. E-Plan | 70° |
| VSWR | ≤1.5 |
| Front to back Ratio | ≥20dB |
| Input Impedance | 50Ω |
| Max Input Power. | 20W |
| Lightning Protection | DC Grounded |
| Mechanical |
| Connector Type | SMA Female |
| Dimensions H*W*D (mm) | 180*180*15(mm) |
| Radome color | Green |
| Operating Temperature Rang | -20ºC/+65ºC |

VSWR:

Radiation Pattern:

BBT ANTENNAS INC

Tel:(8620)38867118  Fax:(8620)38860481   http://www.bbtantennas.com