BBT ANTENNAS INC

Model NO: BBT-2425FG05V

Type : Fiberglass Omni Antenna

Application:

★2.4G antenna access transmission system

★WLAN、WIFI wireless system

★point-to-multipoint coverage transmission system

Features：

★High gain, low VSWR

★High quality fiberglass radome, strong protection

★Strong environmental adaptability

★Standard steel mounting kits

Specifications:

| Electrical |
| --- |
| Model Number | BBT-2425FG05V |
| Frequency Range | 2400-2500MHz |
| Polarization Type | Vertical |
| Gain | 5dBi |
| 3dB Beam-Width. H-Plan | 360° |
| 3dB Beam-Width. E-Plan | 30° |
| VSWR | ≤1.5 |
| Input Impedance | 50Ω |
| Max Input Power. | 50W |
| Lightning Protection | DC Grounded |
| Mechanical |
| Connector Type | N-Type Male |
| Dimensions H*W*D (mm) | Φ20*280（mm） |
| Radome Material | Fiberglass |
| Radome color | gray |
| Operating Temperature Rang | -40ºC/+60ºC |
| Support Pole Diameter | φ30-φ60(mm) |
| Rated Wind Velocity | 60m/s |

VSWR:

Radiation Pattern:

BBT ANTENNAS INC

Tel:(8620)38867118  Fax:(8620)38860481   http://www.bbtantennas.com