BBT ANTENNAS INC

Model NO: BBT-0638WL0708V095

Type : Wall Antenna

Application:

Features：

Specifications:

| Electrical |
| --- |
| Model Number | BBT-0638WL0708V095 |
| Frequency Range | 698-960MHZ | 1710-2700MHZ | 3300-3800MHZ |
| Polarization Type | Vertical |
| Gain | 7dBi | 8dBi | 8dBi |
| 3dB Beam-Width. H-Plan | 95° | 65° | 65° |
| 3dB Beam-Width. E-Plan | 65° | 55° | 55° |
| VSWR | ≤1.7 | ≤1.8 | ≤1.8 |
| Front to Back Ratio(dB) | ≥15dB |
| Input Impedance | 50Ω |
| Max Input Power. | 50W |
| Lightning Protection | DC Grounded |
| Mechanical |
| Connector Type | N-Type Female |
| Cable | RG58U |
| Cable length | 30cm |
| Dimensions H*W*D (mm) | 213*178*44(mm) |
| Weight | 0.58kg |
| Radome Material | ABS |
| Radome color | White |
| Operating Temperature Rang | -40ºC/+60ºC |
| Rated Wind Velocity | 60m/s |

VSWR:

Radiation Pattern:

698-960MHZ

1710-2700MHZ、3300-3800MHZ

BBT ANTENNAS INC

Tel:(8620)38867118  Fax:(8620)38860481   http://www.bbtantennas.com